## Slide 1
ME23312 ENGINEERING THERMODYNAMICS
Unit III – Properties of Pure Substance · Presentation 1 of 10
Pure Substances and their Phases
What Unit III covers · definition of a pure substance · phases and phase changes · why steam is the working fluid · tables and charts instead of pv = RT
Dr. Anantha Raman L., M.E., Ph.D. · Associate Professor, Department of Mechanical Engineering, Rajalakshmi Institute of Technology, Chennai

## Slide 2
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
2
In this presentation
What Unit III covers
What a pure substance is
Examples and non-examples
The three phases
Phase changes
Why steam?
Tables and charts instead of pv = RT

## Slide 3
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
3
What Unit III covers
Formation of steam and its properties; p–v, p–T, T–v, T–s and h–s diagrams; the p–v–T surface
Determination of the dryness fraction
Work and heat transfer in non-flow and flow processes using the steam tables and the Mollier chart
Application of the first and second laws to pure substances
KEY POINT Course outcome CO3: analyse the properties of a pure substance with diagrams and charts to calculate work, heat transfer and dryness fraction.

## Slide 4
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
4
1
Pure substance

## Slide 5
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
5
Definition
A pure substance has a homogeneous and invariable chemical composition throughout its mass – even though it may exist in more than one phase.
Ice, liquid water and steam are all H2O – water and steam together in a boiler drum are still a pure substance

## Slide 6
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
6
Examples and non-examples
Pure substances
Water – ice, liquid, steam, and their mixtures
Nitrogen, oxygen, carbon dioxide, ammonia, refrigerants
Air – as long as its composition does not change
Not pure substances
Air cooled until some of it liquefies – the liquid is richer in oxygen than the vapour, so the phases differ in composition
A mixture of oil and water – not chemically homogeneous

## Slide 7
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
7
2
Phases and phase changes

## Slide 8
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
8
The three phases
Solid
Molecules held in a fixed lattice by strong intermolecular forces; definite shape and volume.
Liquid
Molecules move freely but stay close together; definite volume, no definite shape.
Gas (vapour)
Molecules far apart, moving at random, filling any container. A vapour is a gas near its condensation conditions – steam is water vapour.

## Slide 9
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
9
Phase changes
Change | From → to | Remarks
Melting (fusion) | Solid → liquid | At the melting point
Freezing | Liquid → solid | 
Vaporisation (boiling) | Liquid → vapour | At the saturation temperature for the pressure
Condensation | Vapour → liquid | 
Sublimation | Solid → vapour directly | Below the triple-point pressure: dry ice at 1 atm; ice in a vacuum or on a very cold dry day

## Slide 10
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
10
3
Why steam?

## Slide 11
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
11
Water as the working fluid
Cheap, plentiful, chemically stable and non-toxic
Large latent heat – carries a lot of energy per kilogram
Working fluid of almost all thermal power stations, of process heating in industry, and of many heating and refrigeration systems

## Slide 12
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
12
Tables and charts instead of pv = RT
Steam near its saturation conditions does not obey the ideal-gas equation
Its properties have been measured and are tabulated in the steam tables (IAPWS-97 values in these notes)
They are plotted on charts – the Mollier (h–s) chart is the most used
This unit: how steam forms, how its properties are represented, and how tables and charts give work and heat transfer in closed and open systems

## Slide 13
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
13
Summary
Pure substance: homogeneous, invariable chemical composition, in any number of phases
Water in all its phases, N2, O2, CO2, refrigerants – and air while its composition stays fixed
Phases: solid, liquid, gas; a vapour is a gas near condensation
Phase changes: melting, freezing, vaporisation, condensation, sublimation
Steam: cheap, stable, large latent heat – the universal working fluid
Steam is not an ideal gas – use steam tables and the Mollier chart

## Slide 14
Next: Formation of steam at constant pressure
Compressed liquid → saturated liquid → wet steam → dry saturated → superheated
Saturation temperature and pressure
The T–Q diagram: sensible heat, latent heat and superheat
ME23312 Engineering Thermodynamics · Unit III · Presentation 1
14