## Slide 1
ME23312 ENGINEERING THERMODYNAMICS
Unit III – Properties of Pure Substance · Presentation 2 of 10
Formation of Steam at Constant Pressure
Heating water at constant pressure · compressed liquid, saturated liquid, wet steam, dry saturated and superheated vapour · saturation temperature and pressure · the T–Q diagram · sensible and latent heat
Dr. Anantha Raman L., M.E., Ph.D. · Associate Professor, Department of Mechanical Engineering, Rajalakshmi Institute of Technology, Chennai

## Slide 2
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
2
In this presentation
Heating water at constant pressure
The five states a to e
Saturation temperature and saturation pressure
Fixing the state of wet steam
The T–Q diagram
Sensible heat and latent heat
Latent heat depends on the pressure

## Slide 3
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
3
1
Heating water at constant pressure

## Slide 4
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
4
Formation of steam on the T–v diagram
1 kg of water heated at a constant 0.1 MPa: states a → b → c → d → e; isobars at 0.1, 1 and 10 MPa; the saturation dome

## Slide 5
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
5
States a and b
a Compressed (subcooled) liquid
Water at 30 °C, below its boiling point for the pressure: p > psat(30 °C) = 4.25 kPa (compressed); T < Tsat(0.1 MPa) = 99.6 °C (subcooled). Heating raises T; the volume grows only slightly.
b Saturated liquid
At 99.6 °C the water is about to boil – any further heat begins vaporisation. Properties carry the subscript f: vf, uf, hf, sf.

## Slide 6
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
6
States c and d
c Wet steam
Liquid turns to vapour at constant T and p; the volume grows enormously (0.001043 → 1.694 m³/kg at 0.1 MPa). A two-phase mixture of saturated liquid and saturated vapour in equilibrium.
d Dry saturated vapour
The last drop of liquid has vaporised: vapour at Tsat with no moisture (subscript g: vg, ug, hg, sg), on the point of condensing if heat is removed.

## Slide 7
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
7
State e – superheated vapour
Further heating raises the temperature above the saturation temperature; the temperature and the volume both increase with heat addition.
Superheated steam is fixed by two independent properties, normally p and T

## Slide 8
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
8
2
Saturation temperature and pressure

## Slide 9
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
9
Saturation temperature and saturation pressure
Tsat – the temperature at which a pure substance changes phase at a given pressure
psat – the pressure at which it changes phase at a given temperature
Uniquely related along the vapour-pressure curve: Tsat rises with pressure
Why a pressure cooker cooks faster, and why boiler pressures are raised to reach higher cycle temperatures

## Slide 10
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
10
Boiling point of water against pressure
Pressure | Saturation temperature
0.1 MPa | 99.6 °C
1 MPa | 179.9 °C
10 MPa | 311.0 °C
22.06 MPa (critical) | 374.1 °C

## Slide 11
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
11
Fixing the state of wet steam
During a phase change T and p are not independent – fixing one fixes the other. A single one of them does not fix the state of wet steam.
A second property is needed: v, h, s or the dryness fraction x

## Slide 12
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
12
3
The T–Q diagram
Sensible heat, latent heat and superheat

## Slide 13
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
13
Ice at –10 °C to steam at 150 °C at 1 atm
Temperature of 1 kg of water plotted against the heat supplied

## Slide 14
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
14
Heat supplied: ice at –10 °C → steam at 150 °C
Segment | What happens | Heat (kJ/kg)
A–B | Sensible heat of ice, –10 → 0 °C: cice ΔT = 2.093 × 10 | 20.9
B–C | Latent heat of fusion – ice melts at 0 °C | hsf = 334.5
C–D | Sensible heat of water, 0 → 100 °C: cw ΔT = 4.187 × 100 | 418.7
D–E | Latent heat of vaporisation – water boils at 100 °C | hfg = 2257
E–F | Superheat, 100 → 150 °C: cps ΔT ≈ 2.0 × 50 | ≈ 100
Total |  | ≈ 3131

## Slide 15
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
15
Sensible heat and latent heat
Sensible heat
Produces a change of temperature without a change of phase
Segments A–B, C–D and E–F
Latent heat
Absorbed or released at constant temperature during a change of phase
hsf – latent heat of fusion
hfg = hg – hf – latent heat of vaporisation at constant pressure

## Slide 16
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
16
Latent heat depends on the pressure
hfg = 2257.5 kJ/kg at 0.1 MPa
hfg = 2014.4 kJ/kg at 1 MPa
hfg = 1317.6 kJ/kg at 10 MPa
hfg = 0 at the critical point
KEY POINT Vaporisation is by far the largest item – more than five times the sensible heat of the water.

## Slide 17
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
17
Summary
Constant-pressure heating: compressed liquid → saturated liquid (f) → wet steam → dry saturated vapour (g) → superheated vapour
Volume grows enormously during vaporisation (0.001 → 1.7 m³/kg at 0.1 MPa)
Tsat and psat are uniquely related; Tsat rises with pressure
Wet steam needs a second property (v, h, s or x) to fix its state
Sensible heat changes temperature; latent heat changes phase at constant temperature
hfg falls with pressure and vanishes at the critical point

## Slide 18
Next: Superheat, subcooling, critical and triple points
Degree of superheat and degree of subcooling
Evaporation versus boiling
The critical point and the triple point of water
ME23312 Engineering Thermodynamics · Unit III · Presentation 2
18