## Slide 1
ME23312 ENGINEERING THERMODYNAMICS
Unit III – Properties of Pure Substance · Presentation 3 of 10
Superheat, Subcooling, Evaporation and Boiling, the Critical and Triple Points
Degree of superheat · degree of subcooling · evaporation versus boiling · the critical point and supercritical states · the triple point
Dr. Anantha Raman L., M.E., Ph.D. · Associate Professor, Department of Mechanical Engineering, Rajalakshmi Institute of Technology, Chennai

## Slide 2
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
2
In this presentation
Degree of superheat
Degree of subcooling
Evaporation
Boiling
The critical point
Supercritical states
The triple point

## Slide 3
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
3
1
Degree of superheat and degree of subcooling

## Slide 4
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
4
Degree of superheat
Degree of superheat = T – Tsat(p)
How far superheated steam is above the saturation temperature at the same pressure
Steam at 1.2 MPa and 350 °C: Tsat = 188.0 °C, so the degree of superheat is 162.0 K
Dry saturated steam has zero superheat

## Slide 5
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
5
Degree of subcooling
Degree of subcooling = Tsat(p) – T
How far a compressed liquid is below the saturation temperature at its pressure (also called undercooling)
Water at 1.2 MPa and 40 °C is subcooled by 188.0 – 40 = 148.0 K
A saturated liquid has zero subcooling

## Slide 6
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
6
2
Evaporation and boiling

## Slide 7
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
7
Evaporation versus boiling
Evaporation
At the free surface, at any temperature below the boiling point
The more energetic surface molecules escape into the space above
Slow, no bubbles; rate depends on exposed area, temperature and the vapour already present
Water in an open dish at room temperature; moisture picked up in a cooling tower
Boiling
Vaporisation throughout the bulk of the liquid, with bubble formation
Only when the liquid has reached the saturation temperature for the pressure acting on it
Steam generated in a boiler is produced by boiling

## Slide 8
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
8
3
The critical point

## Slide 9
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
9
Approaching the critical point
As the pressure rises, the horizontal vaporisation segment on the T–v diagram becomes shorter
The saturated liquid expands and the saturated vapour is compressed: vf and vg approach each other, and so do hf and hg
At the critical point the saturated liquid and saturated vapour states coincide

## Slide 10
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
10
The critical point of water
pc = 22.064 MPa, Tc = 373.95 °C (647.1 K), vc ≈ 0.0031 m³/kg
Latent heat is zero: hfg = vfg = sfg = 0
No distinction between liquid and vapour – no meniscus is visible

## Slide 11
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
11
Supercritical states
Above the critical pressure a substance passes from a liquid-like to a gas-like state with no phase change and no boiling
Supercritical boilers work in this region – no drum, no separation of water and steam
The highest-efficiency steam plants operate at supercritical pressures

## Slide 12
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
12
4
The triple point

## Slide 13
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
13
The triple point
The state at which solid, liquid and vapour coexist in equilibrium
A single point on the p–T diagram; a line (the triple line) on the p–v and p–v–T diagrams
Water: Ttp = 0.01 °C (273.16 K exactly), ptp = 0.6117 kPa
The fixed point that defines the Kelvin scale (Unit I)
KEY POINT Below the triple-point pressure a solid sublimes directly to vapour.

## Slide 14
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
14
Summary
Degree of superheat = T – Tsat; zero for dry saturated steam
Degree of subcooling = Tsat – T; zero for saturated liquid
Evaporation: surface, any temperature, slow; boiling: bulk, at Tsat, with bubbles
Critical point of water: 22.064 MPa, 373.95 °C; hfg = 0; liquid and vapour indistinguishable
Supercritical: no phase change, no boiling
Triple point of water: 0.01 °C, 0.6117 kPa – solid, liquid and vapour together

## Slide 15
Next: The p–v–T surface and the p–T diagram
Single-phase and two-phase regions of the p–v–T surface
Substances that contract or expand on freezing
The phase diagram: vaporisation, fusion and sublimation curves
ME23312 Engineering Thermodynamics · Unit III · Presentation 3
15