## Slide 1
ME23312 ENGINEERING THERMODYNAMICS
Unit III – Properties of Pure Substance · Presentation 6 of 10
The Steam Tables
The four tables · compressed liquid approximation · linear interpolation · identifying the state of steam · steam as a real gas
Dr. Anantha Raman L., M.E., Ph.D. · Associate Professor, Department of Mechanical Engineering, Rajalakshmi Institute of Technology, Chennai

## Slide 2
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
2
In this presentation
What the steam tables contain
Saturation tables – temperature and pressure basis
Superheated steam table
Compressed liquid table and the approximation
Linear interpolation
Identifying the state of steam
Steam as a real gas

## Slide 3
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
3
1
The four tables

## Slide 4
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
4
What the steam tables contain
Measured properties of water and steam at saturation and in the superheated region
Values in these notes are from the IAPWS-97 formulation, which textbook tables reproduce to within rounding
Four tables: saturation (temperature basis), saturation (pressure basis), superheated steam, compressed liquid

## Slide 5
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
5
The saturation tables
Temperature basis
For each temperature: psat and vf, vg, uf, ug, hf, hfg, hg, sf, sfg, sg. Used when the temperature of the wet steam or saturated state is known.
Pressure basis
The same properties listed against pressure. Used when the pressure is known – the usual case in boilers, condensers and turbines.

## Slide 6
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
6
Superheat and compressed-liquid tables
Superheated steam table
For each pressure: v, u, h and s at temperatures above Tsat, usually in steps of 50 K; the first row is the saturated vapour. Two independent properties, normally p and T, fix the state.
Compressed liquid table
Properties of liquid water at pressures above the saturation pressure. Where it is not available, treat the compressed liquid as saturated liquid at the same temperature.

## Slide 7
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
7
Compressed liquid approximation
v ≈ vf(T) u ≈ uf(T) s ≈ sf(T)
h ≈ hf(T) + vf (p – psat)
Properties of a liquid depend mainly on temperature, hardly on pressure
The small correction term in h accounts for the flow work at the higher pressure

## Slide 8
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
8
2
Interpolation and identifying the state

## Slide 9
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
9
Linear interpolation
y = y1 + (y2 – y1) (T – T1)/(T2 – T1)
For a property y tabulated as y1 at T1 and y2 at T2, at a temperature T between them
Also used in reverse – to find the temperature (or pressure) at which a property has a given value

## Slide 10
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
10
Identifying the state of steam at a given pressure
Compare the given property with the saturated values at that pressure
v < vf (or T < Tsat) → compressed liquid
vf ≤ v ≤ vg → wet steam – find the dryness fraction x
v > vg (or T > Tsat) → superheated – use the superheat table
KEY POINT The same test works with h, s or u in place of v.

## Slide 11
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
11
3
Steam as a real gas

## Slide 12
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
12
Comparison with the ideal-gas law
Superheated steam at low pressure and high superheat behaves roughly as an ideal gas with R = 8.3145/18.015 = 0.4615 kJ/kg K
Near the saturation line intermolecular attraction reduces the volume below the ideal value; the deviation grows with pressure
At the critical point Z = pv/RT is only 0.23
About 2 % deviation at 1.2 MPa with 162 K of superheat; about 28 % at 10 MPa and 350 °C
KEY POINT Use the steam tables for everything except rough estimates at low pressure.

## Slide 13
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
13
Summary
Saturation tables (T basis and p basis): v, u, h, s of f and g states plus hfg, sfg
Superheat table: v, u, h, s against T for each p; state fixed by (p, T)
Compressed liquid ≈ saturated liquid at the same T; h ≈ hf + vf (p – psat)
Linear interpolation between tabulated entries, forwards or in reverse
Identify the state by comparing v (or h, s, u, T) with the saturated values
Steam is a real gas – pv = RT only for rough low-pressure estimates

## Slide 14
Next: Properties of wet, dry saturated and superheated steam
Dryness fraction and the mixture relations
Internal energy u = h – pv; hfg = Tsat sfg
Numerical problems: Worked Examples 3.1 – 3.4 in the lecture notes
ME23312 Engineering Thermodynamics · Unit III · Presentation 6
14