## Slide 1
ME23312 ENGINEERING THERMODYNAMICS
Unit III – Properties of Pure Substance · Presentation 7 of 10
Properties of Wet, Dry Saturated and Superheated Steam
Dryness fraction · mixture relations for v, h, s and u · validity · finding x from a measured property · dry saturated and superheated steam · hfg = Tsat sfg · internal energy
Dr. Anantha Raman L., M.E., Ph.D. · Associate Professor, Department of Mechanical Engineering, Rajalakshmi Institute of Technology, Chennai

## Slide 2
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
2
In this presentation
Dryness fraction (quality)
Properties of wet steam
Conditions of validity
Finding x from a measured property
Dry saturated steam
Superheated steam
Latent heat and entropy of evaporation
Internal energy of steam

## Slide 3
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
3
1
Wet steam and the dryness fraction

## Slide 4
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
4
Dryness fraction (quality)
x = mg/(mf + mg) 0 ≤ x ≤ 1
wetness fraction = 1 – x = mf/(mf + mg)
Wet steam: saturated liquid + saturated vapour at the same p and Tsat
x = 0 saturated liquid; x = 1 dry saturated vapour; x = 0.9 is "90 % dry" or "10 % wet"

## Slide 5
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
5
Properties of wet steam
Take 1 kg of wet steam: x kg of vapour and (1 – x) kg of liquid
Volume, internal energy, enthalpy and entropy are additive (extensive)
Specific properties of the mixture = mass-weighted averages of the saturated values

## Slide 6
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
6
The mixture relations
v = (1 – x) vf + x vg = vf + x vfg
h = hf + x hfg s = sf + x sfg
u = uf + x ufg = h – pv
vfg = vg – vf, hfg = hg – hf, and so on; at low pressures vf ≪ vg so v ≈ x vg

## Slide 7
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
7
Conditions of validity
Only in the two-phase region, 0 ≤ x ≤ 1
The mixture is at the saturation temperature for its pressure and the phases are in equilibrium
Cannot be used for compressed liquid (x has no meaning) or for superheated vapour – use the corresponding tables

## Slide 8
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
8
Finding x from a measured property
x = (v – vf)/vfg = (h – hf)/hfg = (s – sf)/sfg
Any one of the mixture relations gives x when the mixture property is known
A measured specific volume (rigid vessel of known volume and mass) is the common case

## Slide 9
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
9
2
Dry saturated and superheated steam

## Slide 10
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
10
Dry saturated and superheated steam
Dry saturated (x = 1)
Read vg, ug, hg, sg directly at the given p or T
Superheated (p, T)
Read v, h, s from the superheat table
If u is not tabulated: u = h – pv (p in kPa, v in m³/kg)
Approximation with the mean specific heat cps ≈ 2.0 to 2.1 kJ/kg K: hsup ≈ hg + cps (Tsup – Tsat) – use table values whenever available

## Slide 11
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
11
Latent heat and entropy of evaporation
hfg = Tsat sfg (Tsat in kelvin)
Evaporation is a reversible constant-temperature process, q = T ds
A useful check on table values (Worked Example 3.1)

## Slide 12
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
12
Internal energy of steam
u = h – pv
wet steam: u = (hf + x hfg) – p (vf + x vfg) = uf + x ufg
Enthalpy less the flow (pressure–volume) energy
u is the property for closed-system (non-flow) processes; h is the property for flow processes

## Slide 13
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
13
Summary
x = mg/(mf + mg); wetness = 1 – x
v = vf + x vfg; h = hf + x hfg; s = sf + x sfg; u = uf + x ufg
Valid only for 0 ≤ x ≤ 1 at saturation
x from any measured mixture property, e.g. x = (v – vf)/vfg
Dry saturated: g-values; superheated: (p, T) in the superheat table, u = h – pv
hfg = Tsat sfg; u for closed systems, h for flow

## Slide 14
Next: Determination of the dryness fraction
Barrel, separating, throttling and combined calorimeters
Numerical problems: Worked Examples 3.1 – 3.4 in the lecture notes
ME23312 Engineering Thermodynamics · Unit III · Presentation 7
14