## Slide 1
ME23312 ENGINEERING THERMODYNAMICS
Unit III – Properties of Pure Substance · Presentation 9 of 10
Non-flow Processes of Steam – Work and Heat Transfer
First law for a closed system with steam · constant volume, constant pressure, isothermal, hyperbolic, isentropic and polytropic processes · the four-step procedure · the constant-volume trap
Dr. Anantha Raman L., M.E., Ph.D. · Associate Professor, Department of Mechanical Engineering, Rajalakshmi Institute of Technology, Chennai

## Slide 2
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
2
In this presentation
The first law with steam
The standard non-flow processes
Constant-volume and constant-pressure processes
Isothermal and hyperbolic processes
Isentropic and polytropic processes
The four-step procedure
The constant-volume trap

## Slide 3
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
3
1
The first law with steam

## Slide 4
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
4
Closed systems with steam
Steam in a cylinder or a rigid vessel: Q = ΔU + W, with W = ∫ p dV for a quasi-static process
Unlike an ideal gas, steam has no simple equation of state
Properties at the end states come from the tables; the process relation only fixes the end state and evaluates the work

## Slide 5
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
5
The standard non-flow processes (per kg)
Process | Condition | Work W1–2 | Heat Q1–2
Constant volume | v2 = v1 | 0 | u2 – u1
Constant pressure | p2 = p1 | p (v2 – v1) | h2 – h1
Isothermal | T2 = T1 | q – (u2 – u1) | T (s2 – s1) (reversible)
Hyperbolic | pv = C | p1v1 ln (v2/v1) | (u2 – u1) + W
Isentropic | s2 = s1 | u1 – u2 | 0
Polytropic | pvn = C | (p1v1 – p2v2)/(n – 1) | (u2 – u1) + W

## Slide 6
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
6
2
The processes one by one

## Slide 7
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
7
Constant-volume cooling of superheated steam
A rigid vessel: the steam becomes saturated where the vertical line meets the saturated vapour line (v = vg) and is wet below it

## Slide 8
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
8
Constant volume and constant pressure
Constant volume (rigid vessel)
W = 0, Q = m (u2 – u1)
On cooling, superheated steam becomes saturated when vg(T) = v
Then wet, with x = (v – vf)/vfg
Constant pressure
W = p (V2 – V1), Q = m (h2 – h1)
Boilers and condensers
In the wet region it is also isothermal

## Slide 9
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
9
Constant-pressure heating to superheated steam
Compressed liquid → saturated liquid → dry saturated → superheated on the T–s diagram; Q = area under the curve = h4 – h1

## Slide 10
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
10
Isothermal and hyperbolic processes
Isothermal
Reversible: Q = m T (s2 – s1); W = Q – ΔU
In the wet region identical with constant pressure
In the superheated region p falls as v rises
Hyperbolic, pv = C
W = p1V1 ln (V2/V1); Q = ΔU + W
Not isothermal for steam – only for an ideal gas

## Slide 11
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
11
Isentropic and polytropic processes
Isentropic, s2 = s1
Reversible adiabatic: Q = 0, W = m (u1 – u2)
Ideal expansion in engines
Exit dryness from s2 = sf + x2 sfg
Polytropic, pvn = C
W = (p1V1 – p2V2)/(n – 1); Q = ΔU + W
n ≈ 1.13 for wet steam, 1.3 for superheated steam (Zeuner)
v2 from the process law, then x2 or T2 from the tables

## Slide 12
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
12
3
Procedure and pitfalls

## Slide 13
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
13
The four-step procedure
Fix state 1 from the tables
Use the process condition (v, p, T, s constant or pvn = C) with one given quantity to fix state 2 – decide first whether state 2 is wet or superheated
Read u2, h2, s2
Compute W from the process and Q from the first law; multiply by the mass m

## Slide 14
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
14
The constant-volume trap
In a closed system Q = ΔU + W. Only for a constant-pressure process does Q equal the enthalpy change.
Rigid vessel: W = 0 and Q = ΔU – use u = h – pv, not h2 – h1

## Slide 15
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
15
Summary
Steam has no equation of state – end states from the tables, work from the process law
Constant volume: W = 0, Q = mΔu; constant pressure: W = pΔV, Q = mΔh
Isothermal: Q = mTΔs; hyperbolic: W = p1V1 ln (V2/V1) – not isothermal for steam
Isentropic: Q = 0, W = –mΔu, x2 from s; polytropic: W = (p1V1 – p2V2)/(n – 1)
Procedure: fix state 1 → fix state 2 (wet or superheated?) → read properties → W and Q
Always Q = ΔU + W; Q = ΔH only at constant pressure

## Slide 16
Next: Flow processes and the two laws for steam
Turbine, nozzle, throttling and mixing with the tables and the Mollier chart
Isentropic efficiency, entropy generation and feasibility
Numerical problems: Worked Examples 3.7 – 3.10 in the lecture notes
ME23312 Engineering Thermodynamics · Unit III · Presentation 9
16