## Slide 1
ME23312 ENGINEERING THERMODYNAMICS
Unit III – Properties of Pure Substance · Presentation 10 of 10
Flow Processes of Steam and the Application of the Two Laws
SFEE with steam · turbine and isentropic efficiency · nozzle · throttling · adiabatic mixing · entropy generation and feasibility · availability of steam · Unit III formula sheet
Dr. Anantha Raman L., M.E., Ph.D. · Associate Professor, Department of Mechanical Engineering, Rajalakshmi Institute of Technology, Chennai

## Slide 2
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
2
In this presentation
The SFEE with steam
Steam turbine – ideal and actual
Isentropic efficiency
Steam nozzle
Throttling
Adiabatic mixing of steam streams
First law – closed and open systems
Second law – entropy of steam and feasibility
Availability of steam
Unit III formula sheet

## Slide 3
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
3
1
Flow processes of steam

## Slide 4
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
4
The SFEE with steam
Boilers, turbines, nozzles, condensers, valves and mixing chambers: h1 + V1²/2 + gz1 + q = h2 + V2²/2 + gz2 + w
Enthalpies from the steam tables or the Mollier chart; the potential-energy term is always negligible
The governing property is the enthalpy, not the internal energy
The ideal (reversible adiabatic) process is isentropic – a vertical line on the h–s chart

## Slide 5
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
5
Turbine expansion on the h–s diagram
Isentropic expansion 1–2s is the vertical drop; the actual exhaust 2 lies to the right, with less work and a higher dryness fraction

## Slide 6
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
6
Steam turbine
Insulated casing (q ≈ 0), small velocities: w = h1 – h2
Ideal turbine: s2s = s1; if s1 lies between sf and sg at p2 the exhaust is wet: x2s = (s1 – sf2)/sfg2, h2s = hf2 + x2s hfg2
Ideal work ws = h1 – h2s – the vertical drop on the Mollier chart
Real turbine: friction and turbulence raise the exhaust entropy – state 2 lies to the right of 2s and the work is smaller

## Slide 7
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
7
Isentropic (adiabatic) efficiency of a turbine
ηT = actual work / isentropic work = (h1 – h2)/(h1 – h2s)
h2 = h1 – ηT (h1 – h2s)
Actual exit dryness x2 = (h2 – hf2)/hfg2 is higher than x2s – the energy not converted to work stays in the steam and re-evaporates some moisture
Entropy generated per kg: sgen = s2 – s1 > 0 (adiabatic)

## Slide 8
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
8
Steam nozzle
V2 = √[2 (h1 – h2s)] (h in J/kg)
V2 = 44.72 √(h1 – h2s) (h in kJ/kg, V in m/s)
A2 = ṁ v2/V2, v2 = vf2 + x2 vfg2
Enthalpy drop → kinetic energy; no work, no heat, no change of elevation: V2²/2 – V1²/2 = h1 – h2
Ideal nozzle: isentropic expansion with negligible inlet velocity; nozzle efficiency ηN = (h1 – h2)/(h1 – h2s) for friction

## Slide 9
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
9
Throttling
Partly open valve, orifice or porous plug: large pressure drop, no work, no heat, negligible velocity change ⇒ h1 = h2
A horizontal line on the Mollier chart: wet steam becomes drier and eventually superheated; superheated steam becomes cooler (steam is not an ideal gas)
Highly irreversible: s2 > s1 and the pressure drop is lost
Uses: throttling calorimeter, pressure-reducing valves, refrigerator expansion valve, throttle governing of turbines

## Slide 10
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
10
Adiabatic mixing of steam streams
Two streams at the same pressure mix in an insulated chamber with no work; the mixture may then expand in a nozzle

## Slide 11
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
11
Adiabatic mixing
ṁ1 + ṁ2 = ṁ3 ṁ1h1 + ṁ2h2 = ṁ3h3
h3 = (ṁ1h1 + ṁ2h2)/(ṁ1 + ṁ2)
Mixture state fixed by p and h3: h3 < hg → wet, x3 = (h3 – hf)/hfg; h3 > hg → superheated, T by interpolation
Irreversible: Ṡgen = ṁ3s3 – ṁ1s1 – ṁ2s2 must be positive; desuperheaters and feed-water heaters work this way

## Slide 12
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
12
2
The first and second laws applied to steam

## Slide 13
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
13
First law
Closed systems (non-flow)
Q = m (u2 – u1) + W, W from the process law
u = h – pv, or uf + x ufg for wet steam
Constant V: Q = mΔu; constant p: Q = mΔh; isentropic: W = –mΔu
Open systems (steady flow)
q – w = Δh + ΔV²/2
Turbine w = h1 – h2; nozzle V2 = √[2 (h1 – h2)]
Throttling h1 = h2; boiler, condenser q = h2 – h1; mixing Σ ṁh in = Σ ṁh out

## Slide 14
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
14
Second law – entropy of steam
Entropy is read from the tables (s = sf + x sfg in the wet region), so Δs = s2 – s1 regardless of the path
Reversible process: q = ∫ T ds = area under the T–s curve; isothermal evaporation q = Tsat sfg = hfg
Reversible adiabatic = isentropic; the isentropic end state is the reference for the actual one through the isentropic efficiency

## Slide 15
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
15
Entropy generation and feasibility
Adiabatic device: sgen = sout – sin
Mixing: Ṡgen = Σ ṁoutsout – Σ ṁinsin
Heat q to surroundings at T0: sgen = (s2 – s1) – q/T0
A process is possible only if sgen ≥ 0; the work lost is I = T0 sgen (Unit II)
Throttling generates far more entropy than a real turbine or a mixing chamber – a wasteful way to reduce pressure

## Slide 16
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
16
Availability of steam
ψ = (h – h0) – T0 (s – s0) ηII = w/(ψ1 – ψ2)
Dead state usually taken as saturated liquid at the atmospheric temperature
ψ gives the maximum work obtainable from the stream; the same table values serve both laws

## Slide 17
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
17
Checklist for any steam problem
Fix each state with two independent properties – decide wet, dry or superheated by comparing with the saturation values
Closed system → use u and Q = ΔU + W; open system → use h and the SFEE
Ideal process → s = constant; real process → isentropic efficiency, then the actual end state from h
Test the result with the second law: sgen ≥ 0

## Slide 18
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
18
3
Unit III at a glance
Formula sheet

## Slide 19
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
19
Formula sheet (1) – states and properties
Triple point 0.01 °C, 0.6117 kPa; critical point 22.064 MPa, 373.95 °C, hfg = 0
Degree of superheat T – Tsat; degree of subcooling Tsat – T
x = mg/(mf + mg); v = vf + x vfg; h = hf + x hfg; s = sf + x sfg
u = h – pv = uf + x ufg; hfg = Tsat sfg
Compressed liquid ≈ saturated liquid at the same T; h ≈ hf + vf (p – psat)
Diagrams: T–s heat = area, isentropic vertical; Mollier isentropic vertical, throttling horizontal

## Slide 20
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
20
Formula sheet (2) – calorimeters and processes
Separating x = mg/(mf + mg); throttling x1 = (h2 – hf1)/hfg1
Combined x = x2 m2/(m1 + m2) = x1 x2
Constant volume W = 0, Q = mΔu; constant pressure W = pΔV, Q = mΔh
Isothermal Q = mTΔs; hyperbolic W = p1V1 ln (V2/V1)
Isentropic W = –mΔu; polytropic W = (p1V1 – p2V2)/(n – 1)
Always Q = ΔU + W

## Slide 21
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
21
Formula sheet (3) – flow and the second law
Turbine w = h1 – h2; ηT = (h1 – h2)/(h1 – h2s)
Nozzle V2 = √[2 (h1 – h2)] = 44.72 √Δh; A = ṁv/V
Throttling h1 = h2; mixing h3 = (ṁ1h1 + ṁ2h2)/(ṁ1 + ṁ2)
sgen = s2 – s1 (adiabatic) or Σ ṁsout – Σ ṁsin ≥ 0; I = T0 sgen
Actual turbine exhaust is drier than the isentropic exhaust
ψ = (h – h0) – T0 (s – s0); ηII = w/(ψ1 – ψ2)

## Slide 22
Unit III complete
Numerical problems: Worked Examples 3.1 – 3.15 and Practice Problems P1 – P8 in the lecture notes
Review questions: 30 two-mark and 17 thirteen-mark questions in the notes
Next unit: Ideal and Real Gases, Thermodynamic Relations – Unit IV
ME23312 Engineering Thermodynamics · Unit III · Presentation 10
22