## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 1 • LECTURE 1
Introduction to Thermodynamics: Systems, Properties & Processes
Review of basics — what thermodynamics studies, how we define a system, and the language of properties and processes
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 1 • LECTURE 1
Session Outline
1
Why thermodynamics?
Course overview, real-life applications, CAT pattern for the course
2
System, boundary, surroundings
Definitions with everyday examples
3
Types of systems
Closed, open and isolated systems with mass/energy interaction
4
Properties, state, process, cycle
Intensive vs extensive; point vs path functions
5
Board example + recap
Numerical on absolute / gauge / vacuum pressure; oral questions

## Slide 3
LECTURE 1 • MOTIVATION
Where You Will Meet Thermodynamics
1
Power generation
Steam and gas turbine plants convert heat from fuel into electricity — sized entirely by thermodynamic analysis.
2
IC engines & vehicles
Petrol and diesel engine cycles, efficiency and fuel economy come from the laws you learn in this unit.
3
Refrigeration & air-conditioning
Your fridge and AC pump heat from cold to hot — possible only within second-law limits (Unit II).
4
Aerospace & propulsion
Jet engines and rockets are open systems analysed with the steady flow energy equation (this unit!).
5
Everyday life
Pressure cooker, geyser, bike pump getting warm — all are thermodynamics in action.

## Slide 4
LECTURE 1 • BASIC VOCABULARY
System, Boundary and Surroundings
System — the quantity of matter or region in space chosen for study.
Surroundings — everything external to the system.
Boundary — the real or imaginary surface separating the two.
  The boundary may be fixed (rigid tank) or movable (piston).
  The boundary has zero thickness — it contains no mass.
Choosing the system wisely is the first step of every problem.
SURROUNDINGS
SYSTEM
Boundary (dashed)
Energy in
Energy out
Mass may or may not cross the boundary depending on the type of system
KEY POINT Always draw the system and its boundary before writing any equation — it decides which energies cross.

## Slide 5
LECTURE 1 • CLASSIFICATION
Three Types of Thermodynamic Systems
C
Closed System
Fixed mass — no mass crosses the boundary
Energy (heat / work) CAN cross
Boundary may move (piston–cylinder)
Also called a control mass
Example: gas in a sealed piston–cylinder
O
Open System
Both mass AND energy cross the boundary
Analysed as a control volume with a control surface
Most engineering devices are open systems
Example: turbine, compressor, boiler, nozzle
I
Isolated System
Neither mass nor energy crosses
No interaction with surroundings at all
System + surroundings together form an isolated universe
Example: ideal thermos flask

## Slide 6
LECTURE 1 • PROPERTIES
Intensive vs Extensive Properties
Basis of comparison | Intensive property | Extensive property
Depends on mass? | Independent of mass | Depends on (proportional to) mass
On dividing the system | Value remains the same | Value is halved
Examples | Pressure, Temperature, Density | Volume, Energy, Enthalpy, Entropy
Specific value (per kg) | — (already intensive) | Becomes intensive: v, u, h, s
Symbol convention | p, T, ρ | V, U, H, S (capital letters)
KEY POINT Quick test: mentally cut the system in half — if the value changes, the property is extensive.

## Slide 7
LECTURE 1 • THE LANGUAGE OF CHANGE
State, Process, Path and Cycle — and Two Kinds of Functions
1
State & process
State: the condition described by properties (p, V, T, ...). Process: change from one equilibrium state to another — isobaric, isochoric, isothermal, adiabatic.
2
Path & cycle
Path: the series of states passed through (the curve on the p-V diagram). Cycle: processes returning to the initial state — net change of every property = 0.
3
Point functions
Depend on end states only; exact differentials (dp, dV, dT); ∮ d(property) = 0. All properties are point functions.
4
Path functions
Depend on the path followed; inexact differentials (δQ, δW). Heat and work are NOT properties — a system possesses energy, never "heat" or "work".

## Slide 8
LECTURE 1 • BOARD EXAMPLE
Absolute, Gauge and Vacuum Pressure
PROBLEM A pressure gauge on a compressed-air tank reads 120 kPa, while a vacuum gauge on a condenser reads 66 kPa. The barometer reads 101.3 kPa. Find the absolute pressure in the tank and in the condenser.
Solution
All thermodynamic relations need ABSOLUTE pressure.
Tank (above atmospheric): p_abs = p_atm + p_gauge = 101.3 + 120 = 221.3 kPa
Condenser (below atmospheric): p_abs = p_atm − p_vacuum = 101.3 − 66 = 35.3 kPa
Sanity check: a vacuum reading can never exceed the barometric pressure.
ANSWER
Tank: 221.3 kPa
Condenser: 35.3 kPa
KEY POINT In pV = mRT and all property relations, always substitute absolute pressure — never the gauge reading.

## Slide 9
SESSION 1 • LECTURE 1 • WRAP-UP
Summary & What Comes Next
Today we covered
Thermodynamics = science of energy, heat and work interactions
System / boundary / surroundings vocabulary
Closed vs open vs isolated systems
Intensive vs extensive properties; state, process, path and cycle
p_abs = p_atm + p_gauge; p_abs = p_atm − p_vacuum
NEXT CLASS
Lecture 2 — Thermodynamic Equilibrium & Quasi-static Process
Conditions of equilibrium, and why we idealise processes as infinitely slow.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 1 (Introduction)