## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 2 • LECTURE 2
Thermodynamic Equilibrium & the Quasi-static Process
When is a state truly defined — and how do we idealise real processes so that they can be drawn and integrated?
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 2 • LECTURE 2
Session Outline
1
Recall & connect
Quick questions on systems and properties from Lecture 1
2
Three faces of equilibrium
Thermal, mechanical and chemical equilibrium with examples
3
Quasi-static process
Weight-by-weight compression thought experiment; why infinite slowness
4
Board example
Numerical: piston force balance (mechanical equilibrium)
5
Recap
One-line summaries + preview of displacement work

## Slide 3
LECTURE 2 • CONDITIONS FOR EQUILIBRIUM
The Three Requirements of Thermodynamic Equilibrium
T
Thermal equilibrium
No temperature difference within the system or with surroundings
No heat flow anywhere
Uniform temperature throughout
Driving potential removed: ΔT = 0
M
Mechanical equilibrium
No unbalanced force inside or at the boundary
Pressure is uniform (neglecting gravity gradients)
No macroscopic movement of the boundary
Driving potential removed: Δp = 0
C
Chemical equilibrium
No chemical reaction in progress
No transfer of matter between phases (no diffusion)
Composition is uniform and constant
Driving potential removed: Δμ = 0
KEY POINT A system is in THERMODYNAMIC equilibrium only when all three are satisfied simultaneously.

## Slide 4
LECTURE 2 • WHY EQUILIBRIUM MATTERS
Why Do We Insist on Equilibrium States?
1
Properties need uniformity
A single value of T or p can describe the system only when it is the same everywhere — i.e., at equilibrium.
2
States are points
Only equilibrium states can be plotted as points on p-V, T-s or any property diagram.
3
Non-equilibrium is indescribable
During a fast expansion, pressure differs from place to place — no single point can represent the system.
4
The way out
Perform the process so slowly that the system is always infinitesimally close to equilibrium — the quasi-static idealisation.

## Slide 5
LECTURE 2 • THE CENTRAL IDEALISATION
Quasi-static (Quasi-equilibrium) Process
Definition: a process carried out in such a way that the system passes through a continuous series of equilibrium states.
Classic thought experiment: gas compressed by removing sand grain-by-grain instead of lifting the whole weight at once.
  Each grain causes an infinitesimal disturbance → system re-equilibrates instantly.
  The process is infinitely slow — "quasi" means "almost".
Every intermediate state has well-defined p, V, T.
Hence the full path can be drawn and ∫p dV can be evaluated.
GAS
p, V, T
Piston
dL
δW = p·A·dL = p·dV
KEY POINT Quasi-static is an idealisation — no real process is truly quasi-static, but slow processes come very close.

## Slide 6
LECTURE 2 • CONSEQUENCES
Quasi-static vs Non-quasi-static Processes
Aspect | Quasi-static | Non-quasi-static (rapid)
Intermediate states | All are equilibrium states | Not defined — system is non-uniform
Path on p-V diagram | Continuous solid curve | Only end points; path shown dashed
Work evaluation | W = ∫p dV is valid | ∫p dV cannot be used
Reversibility | Necessary condition for a reversible process | Always irreversible
Example | Slow compression, grain by grain | Bursting of a balloon, free expansion

## Slide 7
LECTURE 2 • BOARD EXAMPLE
Mechanical Equilibrium of a Loaded Piston
PROBLEM A vertical piston–cylinder contains gas. The frictionless piston has a mass of 40 kg and an area of 0.01 m². Atmospheric pressure is 100 kPa and g = 9.81 m/s². Find the gas pressure that holds the piston in equilibrium.
Solution
Force balance on the piston (equilibrium): p_gas A = p_atm A + m g
Weight term as pressure: m g / A = (40 × 9.81) / 0.01 = 39 240 Pa = 39.24 kPa
p_gas = p_atm + mg/A = 100 + 39.24
p_gas = 139.24 kPa — constant as long as the load does not change.
ANSWER
p_gas ≈ 139.2 kPa
KEY POINT A weighted piston fixes the gas pressure — heating such a gas gives a CONSTANT-PRESSURE process. This links directly to tomorrow’s W = pΔV.

## Slide 8
LECTURE 2 • LOOKING AHEAD
Reversible Process — a First Look
1
Definition
A process that can be reversed leaving no trace on the surroundings — both system and surroundings return to their initial states.
2
Requirement 1: quasi-static
The system must always be in equilibrium so that each step can be exactly retraced.
3
Requirement 2: no dissipative effects
No friction, no unrestrained expansion, no heat transfer across a finite temperature difference.
4
Why we care
Reversible processes give the maximum work output / minimum work input — the benchmark used throughout Units II–V.

## Slide 9
SESSION 2 • LECTURE 2 • WRAP-UP
Summary & What Comes Next
Today we covered
Thermodynamic equilibrium = thermal + mechanical + chemical equilibrium together
Properties are defined only at equilibrium states
A quasi-static process is a succession of equilibrium states (infinitely slow)
Only quasi-static paths can be drawn as continuous curves on a p-V diagram
Piston equilibrium: p_gas = p_atm + weight/(A) — force balance sets the gas pressure
NEXT CLASS
Lecture 3 — Displacement Work & the p-V Diagram
We derive W = ∫p dV and learn to read work as area under the curve.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 1 (Introduction)