## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 3 • LECTURE 3
Displacement Work and the p-V Diagram
Deriving W = ∫p dV, reading work as area under the curve, and work expressions for standard processes
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 3 • LECTURE 3
Session Outline
1
Recall & connect
Quasi-static recap; sign convention for heat and work
2
Derivation of δW = p dV
Piston–cylinder force analysis, step by step
3
Work as area on p-V diagram
Path dependence demonstrated with different curves
4
Work in standard processes
Constant V, constant p, isothermal (pV = C), polytropic (pVⁿ = C)
5
Board example + recap
Finding the polytropic index n from two states, then the work

## Slide 3
LECTURE 3 • GROUND RULES
Work Transfer and the Sign Convention
1
Thermodynamic definition of work
Work is done by a system if the sole effect on the surroundings could be reduced to the raising of a weight.
2
Sign convention (used throughout this course)
Work done BY the system → positive. Work done ON the system → negative. Heat TO the system → positive; heat rejected → negative.
3
Units
Work and heat are energy in transit: joule (J), kilojoule (kJ). Rate of work = power, watt (W).
4
Boundary (displacement) work
The work associated with a moving boundary — the most common form in piston–cylinder devices.

## Slide 4
LECTURE 3 • DERIVATION
Displacement Work: δW = p dV
Gas at pressure p pushes piston of area A.
  Force on piston: F = p × A
  Piston moves a small distance dL.
  Work done: δW = F × dL = p × A × dL
But A × dL = dV (change in volume), so δW = p dV.
Total work for process 1→2: W₁₂ = ∫₁² p dV
Valid only for a quasi-static process, where p is defined at every instant.
GAS
p, V, T
Piston
dL
δW = p·A·dL = p·dV

## Slide 5
LECTURE 3 • GRAPHICAL MEANING
Work is the Area Under the p-V Curve
Chart: Volume V (m³)
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
Constant pressure | 300 | 300 | 300 | 300 | 300 | 300 | 300
Isothermal pV = C | 600 | 400 | 300 | 240 | 200 | 171.4286 | 150
Polytropic pV¹·³ = C | 600 | 354.187 | 243.6757 | 182.3179 | 143.8446 | 117.7234 | 98.9631
Read the diagram
Area under the curve between V₁ and V₂ equals ∫p dV — the displacement work.
Different curves joining the same two states enclose different areas.
Hence work depends on the PATH — it is a path function.
Steeper fall of p (higher n) → smaller area → less work.

## Slide 6
LECTURE 3 • FORMULA SHEET
Displacement Work for Standard Quasi-static Processes
Process | p–V relation | Work done W₁₂
Constant volume (isochoric) | V = constant | W = 0
Constant pressure (isobaric) | p = constant | W = p (V₂ − V₁)
Isothermal (ideal gas) | pV = constant | W = p₁V₁ ln(V₂/V₁) = mRT ln(V₂/V₁)
Polytropic | pVⁿ = constant (n ≠ 1) | W = (p₁V₁ − p₂V₂)/(n − 1)
Adiabatic (special polytropic) | pV^γ = constant | W = (p₁V₁ − p₂V₂)/(γ − 1)
KEY POINT These five results answer 80% of Unit-I numericals — the tutorial next class drills all of them.

## Slide 7
LECTURE 3 • BOARD EXAMPLE
Finding the Polytropic Index from Two States
PROBLEM A gas expands from 5 bar, 0.1 m³ to 1 bar, 0.4 m³ following pVⁿ = constant. Determine the index n and the work done.
Solution
p₁V₁ⁿ = p₂V₂ⁿ ⇒ (p₁/p₂) = (V₂/V₁)ⁿ
n = ln(p₁/p₂) / ln(V₂/V₁) = ln 5 / ln 4 = 1.609 / 1.386 = 1.161
W = (p₁V₁ − p₂V₂)/(n − 1) with p in kPa: (500×0.1 − 100×0.4)/(0.161)
W = (50 − 40)/0.161 = 62.1 kJ
Positive → expansion work done by the gas. ✓
ANSWER
n ≈ 1.16
W ≈ + 62.1 kJ
KEY POINT When both end states are given, extract n first from the logs — a favourite CAT sub-question.

## Slide 8
LECTURE 3 • CAUTION
When ∫p dV Fails, and Other Work Modes
1
Free (unrestrained) expansion
Gas expanding into vacuum: no resisting force, so W = 0 even though volume increases. ∫p dV must NOT be applied — process is not quasi-static.
2
Rapid processes
p is non-uniform during fast expansion or compression; the integral has no meaning.
3
Other quasi-static work modes
Shaft work (paddle wheel), electrical work (∫VI dt), spring work, stretching of a wire, surface film — same sign convention applies.
4
Net work
W_net = W_displacement + W_shaft + W_electrical + ... — add every mode crossing the boundary.

## Slide 9
SESSION 3 • LECTURE 3 • WRAP-UP
Summary & What Comes Next
Today we covered
Sign convention: W done BY the system is positive; Q supplied TO the system is positive
δW = p dV for a quasi-static process; W = area under the p-V curve
Work is a path function — different paths give different work
Formulas: W = 0 (const V), p(V₂−V₁) (const p), p₁V₁ ln(V₂/V₁) (isothermal), (p₁V₁−p₂V₂)/(n−1) (polytropic)
Index from states: n = ln(p₂/p₁) / ln(V₁/V₂)
NEXT CLASS
Tutorial 1 — Problems on Displacement Work
Four problems solved step by step on the board. Bring your calculator.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 3 (Work and Heat Transfer)