## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 4 • TUTORIAL 1
Tutorial 1: Problems on Displacement Work & p-V Diagram
Four worked problems on the board + additional practice problems with answers
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 4 • TUTORIAL 1
Session Outline
1
Formula recall
One-minute review of the five work formulas
2
Problem 1 — constant pressure
Direct application of W = pΔV with unit conversion
3
Problem 2 — polytropic process
Finding p₂ from pVⁿ = C, then work
4
Problem 3 — isothermal process
Logarithmic work formula in mass form
5
Problem 4 + recap
Two-step process (p = C then V = C); key takeaways

## Slide 3
TUTORIAL 1 • WORKED PROBLEM 1
Constant Pressure Expansion
PROBLEM A gas expands at a constant pressure of 3 bar from a volume of 0.05 m³ to 0.20 m³. Determine the work done by the gas.
Solution
Identify the process: constant pressure → W = p (V₂ − V₁)
Convert pressure to SI: p = 3 bar = 3 × 100 kPa = 300 kPa
ΔV = V₂ − V₁ = 0.20 − 0.05 = 0.15 m³
W = 300 kPa × 0.15 m³ = 45 kJ
W is positive → expansion; work is done BY the gas on the surroundings.
ANSWER
W = + 45 kJ
KEY POINT 1 bar = 100 kPa = 10⁵ Pa. kPa × m³ gives kJ directly — the cleanest unit set.

## Slide 4
TUTORIAL 1 • WORKED PROBLEM 2
Polytropic Compression
PROBLEM Air (0.3 m³ at 1 bar) is compressed following pV¹·³ = constant to a final volume of 0.05 m³. Find the final pressure and the work done.
Solution
Final pressure: p₂ = p₁ (V₁/V₂)ⁿ = 1 × (0.3/0.05)¹·³ = 6¹·³ = 10.27 bar
Convert: p₁ = 100 kPa, p₂ = 1027 kPa
W = (p₁V₁ − p₂V₂)/(n − 1) = (100×0.3 − 1027×0.05)/(1.3 − 1)
W = (30 − 51.35)/0.3 = −21.35/0.3 = −71.2 kJ
Negative sign → work is done ON the air (compression), as expected.
ANSWER
p₂ ≈ 10.27 bar
W ≈ − 71.2 kJ
KEY POINT For compression V₂ < V₁, the numerator turns negative automatically — never force the sign by hand.

## Slide 5
TUTORIAL 1 • WORKED PROBLEM 3
Isothermal Expansion
PROBLEM 0.5 kg of air (R = 0.287 kJ/kg·K) at 400 K expands isothermally until its volume doubles. Calculate the work done.
Solution
Isothermal ideal gas: W = mRT ln(V₂/V₁)
V₂/V₁ = 2 → ln 2 = 0.6931
W = 0.5 × 0.287 × 400 × 0.6931
W = 57.4 × 0.6931 = 39.79 kJ
Check: expansion → W positive. For an ideal gas at constant T, Q = W (preview of the first law!).
ANSWER
W ≈ + 39.8 kJ
KEY POINT mRT has units kJ when R is in kJ/kg·K — keep R in kJ throughout this course.

## Slide 6
TUTORIAL 1 • WORKED PROBLEM 4
Work in a Two-step Process
PROBLEM A gas at 1 bar, 0.10 m³ is (i) heated at constant pressure until its volume becomes 0.30 m³, then (ii) heated at constant volume until its pressure becomes 3 bar. Find the total work done and sketch the p-V diagram.
Solution
Step (i), constant p: W₁ = pΔV = 100 kPa × (0.30 − 0.10) = 20 kJ
Step (ii), constant V: W₂ = 0 (no volume change — vertical line on p-V)
Total: W = W₁ + W₂ = 20 + 0 = 20 kJ
p-V sketch: horizontal line (1→2) then vertical line (2→3); area lies only under the horizontal part.
ANSWER
W_total = + 20 kJ
KEY POINT In multi-step problems, work comes only from steps where the volume changes.

## Slide 7
TUTORIAL 1 • MORE PRACTICE
Additional Practice Problems — Answers Provided
P1
Constant pressure + piston
A piston–cylinder holds 0.1 m³ of gas at 2 bar. Heat is added until the volume becomes 0.25 m³ at constant pressure. Find the work done. [Ans: 30 kJ]
P2
Polytropic expansion
A gas at 8 bar, 0.02 m³ expands to 1 bar following pV¹·⁴ = C. Find V₂ and the work done. [Ans: V₂ ≈ 0.0885 m³, W ≈ +17.9 kJ]
P3
Free expansion (concept trap)
A vessel is divided by a partition: gas on one side, vacuum on the other. The partition is removed. How much displacement work is done? Justify. [Ans: W = 0 — no resisting pressure]
✓
Presentation checklist
Draw the p-V sketch → state the process law → list given data in SI → formula → substitute → box the answer with sign and unit.

## Slide 8
SESSION 4 • TUTORIAL 1 • WRAP-UP
Summary & What Comes Next
Today we covered
Convert every quantity to SI before substituting (bar → kPa: ×100)
Identify the process first — the process picks the formula
Polytropic: get the unknown end state from p₁V₁ⁿ = p₂V₂ⁿ before computing W
Multi-step processes: compute W for each step and add algebraically
Sketch the p-V diagram for every problem — it earns marks
NEXT CLASS
Lecture 4 — Thermal Equilibrium, Zeroth Law & Temperature
Why the thermometer works: the zeroth law and thermometric properties.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 3 (Work and Heat Transfer)