## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 5 • LECTURE 4
Thermal Equilibrium, Zeroth Law & the Concept of Temperature
The law that makes thermometry possible — and why it is numbered zero
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 5 • LECTURE 4
Session Outline
1
Recall & connect
Discussion of common errors from the tutorial problems
2
Thermal equilibrium revisited
Heat flow stops when temperatures equalise
3
Zeroth law of thermodynamics
Statement, diagram with bodies A, B, C, and its meaning
4
Temperature & thermometric properties
How the law leads to temperature measurement; types of thermometers
5
Board example + recap
Numerical on a resistance thermometer (linear thermometric property)

## Slide 3
LECTURE 4 • FOUNDATION
Thermal Equilibrium — the Physical Picture
1
Hot coffee in a room
Heat flows from coffee (higher T) to air (lower T). The flow continues as long as a temperature difference exists.
2
Approach to equilibrium
The temperature difference — the driving potential — shrinks until it vanishes. Then heat flow stops.
3
Definition
Two systems are in thermal equilibrium when, on being brought into communication through a diathermic (heat-conducting) wall, no change of any property occurs.
4
Walls
Diathermic wall: permits heat flow (thin copper sheet). Adiabatic wall: prevents heat flow (thick insulation).

## Slide 4
LECTURE 4 • THE LAW ITSELF
Zeroth Law of Thermodynamics
Statement: if body A is in thermal equilibrium with body C, and body B is separately in thermal equilibrium with body C, then A and B are in thermal equilibrium with each other.
Formulated by R.H. Fowler in 1931 — after the first and second laws were named, yet logically prior to both. Hence "zeroth".
C is the go-between: it is the thermometer.
  A and B need never touch each other.
The common property shared at equilibrium is what we call temperature.
BODY C
(Thermometer)
BODY A
BODY B
A = C and B = C ⇒ A = B (thermal equilibrium)
KEY POINT The zeroth law is the logical foundation of ALL temperature measurement.

## Slide 5
LECTURE 4 • INSTRUMENTS
Common Thermometers and Their Thermometric Properties
Thermometer | Thermometric property | Typical range / remark
Mercury / alcohol in glass | Length of liquid column, L | −38 to 350 °C; simple, direct reading
Constant-volume gas thermometer | Pressure of a fixed gas volume, p | Very wide range; the standard instrument
Electrical resistance (RTD) | Resistance of platinum wire, R | −200 to 850 °C; high accuracy
Thermocouple | Thermo-emf between junctions, ε | Wide range; fast response; remote sensing
Ideal-gas connection | p at constant V → T = 273.16 (p/p_tp) | Basis of the absolute Kelvin scale (next class)
KEY POINT On a two-point scale, any property x gives: t = 100 (x − x_ice)/(x_steam − x_ice) °C.

## Slide 6
LECTURE 4 • BOARD EXAMPLE
Resistance Thermometer (Linear Thermometric Property)
PROBLEM The resistance of a platinum wire is 10.00 Ω at the ice point and 13.86 Ω at the steam point. Assuming resistance varies linearly with temperature, find the temperature when the resistance reads 12.40 Ω.
Solution
Linear two-point scale: t = 100 × (R − R_ice)/(R_steam − R_ice)
R − R_ice = 12.40 − 10.00 = 2.40 Ω
R_steam − R_ice = 13.86 − 10.00 = 3.86 Ω
t = 100 × 2.40/3.86 = 62.2 °C
ANSWER
t ≈ 62.2 °C
KEY POINT Nag Ch. 2 pattern: the same formula works for ANY linear thermometric property — length, pressure, emf or resistance.

## Slide 7
SESSION 5 • LECTURE 4 • WRAP-UP
Summary & What Comes Next
Today we covered
Two bodies in thermal equilibrium have no net heat flow between them
Zeroth law: if A ≡ C and B ≡ C, then A ≡ B
It gives temperature its meaning: equal temperature ⇔ thermal equilibrium
Body C acts as the thermometer; a thermometric property varies measurably with T
Linear property: t = 100 (x − x_ice)/(x_steam − x_ice) on the two-point Celsius scale
NEXT CLASS
Lecture 5 — Temperature Scales
Celsius, Fahrenheit, Kelvin, Rankine and the ideal-gas absolute scale.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 2 (Temperature)