## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 6 • LECTURE 5
Temperature Scales
Celsius, Fahrenheit, Kelvin, Rankine — relationships, conversions and the ideal-gas absolute scale
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 6 • LECTURE 5
Session Outline
1
Recall & connect
Zeroth law recap; why we need agreed scales
2
The four scales
Fixed points and relations: °C, °F, K, °R
3
Conversion practice
Quick conversions solved with the class
4
Ideal-gas (absolute) scale
Constant-volume gas thermometer; T = 273.16 (p/p_tp)
5
Board example + recap
Numerical on an arbitrary scale °N vs °C

## Slide 3
LECTURE 5 • THE FOUR SCALES
Temperature Scales at a Glance
Feature | Celsius (°C) | Fahrenheit (°F) | Kelvin (K) | Rankine (°R)
Type | Relative | Relative | Absolute (SI) | Absolute (English)
Ice point of water | 0 | 32 | 273.15 | 491.67
Steam point of water | 100 | 212 | 373.15 | 671.67
Absolute zero | −273.15 | −459.67 | 0 | 0
Divisions (ice→steam) | 100 | 180 | 100 | 180

## Slide 4
LECTURE 5 • CONVERSION FORMULAS
The Only Four Relations You Need
T(K) = T(°C) + 273.15
Celsius → Kelvin (use 273 in problems unless asked)
T(°F) = 1.8 × T(°C) + 32
Celsius → Fahrenheit
T(°R) = T(°F) + 459.67
Fahrenheit → Rankine
ΔT(K) = ΔT(°C) ΔT(°R) = ΔT(°F) = 1.8 ΔT(K)
Differences: °C and K intervals are identical
Worked micro-examples
25 °C = 25 + 273.15 = 298.15 K (room temperature)
98.6 °F = (98.6 − 32)/1.8 = 37 °C = 310.15 K (body temperature)
A rise of 20 °C is a rise of 20 K — never add 273 to a difference!
KEY POINT In pV = mRT, Carnot efficiency, entropy — every thermodynamic formula — T must be in kelvin.

## Slide 5
LECTURE 5 • THE STANDARD SCALE
Ideal-gas (Absolute) Temperature Scale
1
Instrument
Constant-volume gas thermometer: a fixed volume of gas whose pressure is read at the unknown temperature and at the triple point of water.
2
Defining relation
T = 273.16 × (p / p_tp) at constant volume, where 273.16 K is assigned to the triple point of water.
3
Gas-independence
As the amount of gas is reduced (p_tp → 0), all gases give the SAME temperature — the ideal-gas scale, independent of the gas used.
4
Link to thermodynamics
The ideal-gas scale coincides with the thermodynamic (Kelvin) scale defined later from the second law — that is why K is "absolute".
KEY POINT Absolute zero (0 K) is the temperature at which an ideal gas would exert zero pressure — unattainable in practice.

## Slide 6
LECTURE 5 • BOARD EXAMPLE
An Arbitrary Temperature Scale °N
PROBLEM On a new scale N, the ice point is marked 20 °N and the steam point 220 °N. (i) What is the °N reading at 60 °C? (ii) At what temperature do the °N and °C readings coincide?
Solution
Linear relation: t_N = a t_C + b. Ice: 20 = b. Steam: 220 = 100a + 20 ⇒ a = 2
So t_N = 2 t_C + 20
(i) At 60 °C: t_N = 2×60 + 20 = 140 °N
(ii) Coincide: t = 2t + 20 ⇒ t = −20
Readings agree at −20° on both scales (like −40° for °C and °F).
ANSWER
(i) 140 °N
(ii) −20°
KEY POINT Every "new scale" problem is a straight line through two fixed points — find slope and intercept first.

## Slide 7
SESSION 6 • LECTURE 5 • WRAP-UP
Summary & What Comes Next
Today we covered
K = °C + 273.15; °R = °F + 459.67; °F = 1.8(°C) + 32; °R = 1.8 K
A temperature DIFFERENCE is identical in °C and K (and in °F and °R)
Thermodynamic relations always use ABSOLUTE temperature (K)
Ideal-gas scale: T = 273.16 × (p/p_tp) at constant volume, extrapolated to low pressure
Arbitrary scale problems: fit t_N = a t_C + b through the two fixed points
NEXT CLASS
Lecture 6 — First Law for Closed Systems
Joule’s experiment, ∮δQ = ∮δW, internal energy and Q − W = ΔU.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 2 (Temperature)