## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 7 • LECTURE 6
First Law of Thermodynamics — Closed Systems
Joule’s experiment, the cyclic statement ∮δQ = ∮δW, internal energy, and Q − W = ΔE
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 7 • LECTURE 6
Session Outline
1
Recall & connect
Heat and work as boundary interactions; path functions
2
Joule’s paddle-wheel experiment
Work in, heat out — the fixed ratio that founded the first law
3
First law statements
For a cycle: ∮δQ = ∮δW. For a process: Q − W = ΔE
4
Internal energy & PMM1
Why E is a property; specific heats c_v, c_p
5
Two board examples
Energy balance for expansion and for compression

## Slide 3
LECTURE 6 • THE FOUNDING EXPERIMENT
Joule’s Paddle-Wheel Experiment (1843–48)
Insulated water tank; falling weight spins a paddle wheel, stirring the water.
  Measured work input W (weight × drop height) raises water temperature.
  System then cooled back to initial state by heat transfer Q to surroundings.
Finding: W/Q is always the SAME constant, whatever the amounts.
In SI both are in joules: net work in = net heat out for the cycle.
Conclusion: heat and work are interchangeable forms of energy.
SURROUNDINGS
SYSTEM
Boundary (dashed)
Energy in
Energy out
Mass may or may not cross the boundary depending on the type of system
KEY POINT Joule’s constant (4.186 kJ/kcal) unified heat and work into one currency: energy.

## Slide 4
LECTURE 6 • THE LAW
First Law — Cycle Form and Process Form
∮ δQ = ∮ δW
For a closed system undergoing a CYCLE: net heat transfer = net work transfer
Q₁₂ − W₁₂ = ΔE = E₂ − E₁
For a PROCESS 1→2: energy is conserved; the difference is stored
From cycle form to process form
Consider two processes A and B between states 1 and 2 forming a cycle: (Q − W) along A equals (Q − W) along B.
(Q − W) is therefore path-independent → it defines a property: the total energy E.
E = U + KE + PE. In most stationary closed systems ΔKE = ΔPE = 0, so:
Q − W = ΔU (working form for closed-system problems)
KEY POINT Energy can be neither created nor destroyed during a process; it can only change forms.

## Slide 5
LECTURE 6 • THE NEW PROPERTY
Internal Energy U — and the Specific Heats
1
What is U?
The sum of all microscopic energies — molecular translation, rotation, vibration, and intermolecular potential energy. An extensive property; u = U/m.
2
U is a point function
ΔU between two states is the same for every path — unlike Q and W individually. Only their difference is fixed.
3
Specific heat at constant volume
c_v = (∂u/∂T)_v. For a constant-volume process of an ideal gas: Q = ΔU = m c_v ΔT (since W = 0).
4
Specific heat at constant pressure
c_p = (∂h/∂T)_p. For constant pressure: Q = m c_p ΔT; the extra (c_p − c_v) supplies the boundary work. c_p − c_v = R for an ideal gas.
5
Ideal-gas shortcut
For an ideal gas u = u(T) only (Joule’s law) → ΔU = m c_v ΔT for ANY process, not just constant volume.

## Slide 6
LECTURE 6 • BOARD EXAMPLE 1
Applying Q − W = ΔU
PROBLEM During a process, 80 kJ of heat is supplied to a closed system while the system does 30 kJ of work on the surroundings. Find the change in internal energy. If the system is then restored to its initial state adiabatically, how much work is involved?
Solution
Process 1→2: Q = +80 kJ (supplied), W = +30 kJ (done by system)
ΔU₁₂ = Q − W = 80 − 30 = +50 kJ → internal energy rises by 50 kJ
Return process 2→1 (adiabatic): Q = 0, and ΔU₂₁ = U₁ − U₂ = −50 kJ
First law: 0 − W₂₁ = ΔU₂₁ = −50 ⇒ W₂₁ = +50 kJ
Interpretation: the 50 kJ stored in process 1→2 leaves entirely as work output during the adiabatic return.
ANSWER
ΔU₁₂ = +50 kJ
W₂₁ = +50 kJ (by system)
KEY POINT Write Q − W = ΔU, substitute with signs, and let the algebra decide the direction.

## Slide 7
LECTURE 6 • BOARD EXAMPLE 2
Compression with Heat Rejection
PROBLEM A gas is compressed in a piston–cylinder: the work done ON the gas is 95 kJ, and 43 kJ of heat is rejected to the surroundings during the process. Determine the change in internal energy of the gas.
Solution
Assign signs: W = −95 kJ (done ON the system), Q = −43 kJ (rejected)
First law: ΔU = Q − W
ΔU = (−43) − (−95) = −43 + 95
ΔU = +52 kJ → internal energy increases (compression heats the gas more than cooling removes).
ANSWER
ΔU = + 52 kJ
KEY POINT Two negatives are common in compression problems — substitute mechanically and trust the signs.

## Slide 8
SESSION 7 • LECTURE 6 • WRAP-UP
Summary & What Comes Next
Today we covered
First law = principle of conservation of energy for thermodynamic systems
For a cycle: ∮δQ = ∮δW (net heat = net work)
For a process: Q − W = ΔE; with KE, PE negligible, Q − W = ΔU
Internal energy U is a property (point function); Q and W are not
For an ideal gas: ΔU = m c_v ΔT for ANY process; PMM1 is impossible
NEXT CLASS
Tutorial 2 — First Law: Closed System Problems
Energy-balance numericals for processes and complete cycles.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 4 (First Law of Thermodynamics)