## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 8 • TUTORIAL 2
Tutorial 2: First Law Applied to Closed Systems
Energy balances for single processes, cycles and paddle-wheel work
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 8 • TUTORIAL 2
Session Outline
1
Statement recall
Q − W = ΔU and the cycle form, sign conventions
2
Problem 1 — single process
Direct energy balance with mixed signs
3
Problem 2 — cycle of three processes
Completing the energy-balance table for a cycle
4
Problem 3 — constant pressure with c_p
Heat, work and ΔU in one problem
5
Problem 4 + recap
Paddle-wheel work in an insulated vessel; key takeaways

## Slide 3
TUTORIAL 2 • WORKED PROBLEM 1
Energy Balance for a Single Process
PROBLEM A closed system receives 200 kJ of heat. During the process the system does 80 kJ of work on the surroundings, and 30 kJ of heat is lost to the casing. Determine the change in internal energy.
Solution
Net heat: Q = +200 − 30 = +170 kJ
Work by system: W = +80 kJ
First law: ΔU = Q − W = 170 − 80
ΔU = +90 kJ → internal energy increases by 90 kJ
ANSWER
ΔU = + 90 kJ
KEY POINT Sum ALL heat interactions (with signs) before applying the balance.

## Slide 4
TUTORIAL 2 • WORKED PROBLEM 2
A Complete Cycle — Fill the Energy Table
PROBLEM A closed system undergoes a cycle of three processes. Given: Q₁₂ = +40 kJ, W₁₂ = +15 kJ; Q₂₃ = −10 kJ, W₂₃ = 0; W₃₁ = −20 kJ. Find ΔU for each process and Q₃₁.
Process | Q (kJ) | W (kJ) | ΔU = Q − W (kJ)
1 → 2 | +40 | +15 | +25
2 → 3 | −10 | 0 | −10
3 → 1 | Q₃₁ = −35 | −20 | −15 (so that ΣΔU = 0)
Σ (cycle) | −5 | −5 | 0 ✓
Reasoning: over the cycle ΣΔU = 0 ⇒ ΔU₃₁ = −(25 − 10) = −15 kJ. Then Q₃₁ = ΔU₃₁ + W₃₁ = −15 + (−20) = −35 kJ.
Verification: ΣQ = 40 − 10 − 35 = −5 kJ = ΣW = 15 + 0 − 20 = −5 kJ ✓ (net work-absorbing cycle).

## Slide 5
TUTORIAL 2 • WORKED PROBLEM 3
Constant-Pressure Heating of Air
PROBLEM 2 kg of air (c_p = 1.005, c_v = 0.718 kJ/kg·K, R = 0.287 kJ/kg·K) is heated at constant pressure from 300 K to 450 K. Find Q, W and ΔU.
Solution
Q = m c_p ΔT = 2 × 1.005 × 150 = 301.5 kJ
ΔU = m c_v ΔT = 2 × 0.718 × 150 = 215.4 kJ
W = Q − ΔU = 301.5 − 215.4 = 86.1 kJ
Check: W = mRΔT = 2 × 0.287 × 150 = 86.1 kJ ✓
ANSWER
Q = 301.5 kJ
ΔU = 215.4 kJ
W = 86.1 kJ
KEY POINT The consistency check W = mRΔT catches arithmetic slips instantly — use it in the CAT.

## Slide 6
TUTORIAL 2 • WORKED PROBLEM 4
Paddle-Wheel Work in an Insulated Vessel
PROBLEM A rigid, insulated vessel contains 2 kg of air (c_v = 0.718 kJ/kg·K). A paddle wheel driven by an external motor does 25 kJ of work on the air. Find the change in internal energy and the temperature rise.
Solution
Rigid → no displacement work; insulated → Q = 0
Paddle work is done ON the system: W = −25 kJ
ΔU = Q − W = 0 − (−25) = +25 kJ
ΔT = ΔU / (m c_v) = 25 / (2 × 0.718) = 17.4 K
ANSWER
ΔU = +25 kJ
ΔT ≈ 17.4 K
KEY POINT Shaft/paddle work bypasses the boundary-work formula — it always enters the balance directly as W.

## Slide 7
TUTORIAL 2 • MORE PRACTICE
Additional Practice Problems — Answers Provided
P1
Mixed interactions
A system receives 120 kJ of heat and 40 kJ of paddle-wheel work while doing 65 kJ of expansion work. Find ΔU. [Ans: +95 kJ]
P2
Cycle completion
A cycle has two processes: A (Q = +50 kJ, W = +20 kJ) and B (W = −15 kJ). Find Q for process B and the net work of the cycle. [Ans: Q_B = −45 kJ; W_net = +5 kJ]
✱
Concept check
True or false: "In an adiabatic process the internal energy always remains constant." Justify in two lines. [False — ΔU = −W]
✓
CAT-I pointer
CAT-I covers Units I & II. A 13-mark question from first-law closed systems is a regular feature — practise the table method for cycles.

## Slide 8
SESSION 8 • TUTORIAL 2 • WRAP-UP
Summary & What Comes Next
Today we covered
Always write the balance Q − W = ΔU with algebraic signs, then substitute
Over a complete cycle ΣΔU = 0, hence ΣQ = ΣW
Constant pressure: Q = m c_p ΔT; W = pΔV = mRΔT; ΔU = m c_v ΔT
Paddle work enters as negative W (work ON the system)
Tabulate Q, W, ΔU per process for cycle problems — fastest and safest
NEXT CLASS
Lecture 7 — First Law for Open Systems: SFEE
Control volumes, flow work, enthalpy and the steady flow energy equation.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 4 (First Law of Thermodynamics)