## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 9 • LECTURE 7
First Law for Open Systems — The Steady Flow Energy Equation
Control volumes, flow work, enthalpy, and the derivation of the SFEE
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 9 • LECTURE 7
Session Outline
1
Recall & connect
Closed vs open systems — quick recap
2
Control volume & flow work
Why pushing mass across a boundary costs pv per kg
3
Enthalpy
h = u + pv — the natural energy currency of flowing fluids
4
SFEE derivation
Energy bookkeeping across the control surface, term by term
5
Board example + recap
Numerical: computing h and flow work for steam

## Slide 3
LECTURE 7 • NEW SYSTEM TYPE
Control Volume and Control Surface
Most real devices — turbines, pumps, boilers — have mass flowing through them: closed-system analysis cannot apply.
Control volume (CV): a fixed region in space chosen for study.
  Control surface (CS): its boundary — mass, heat and work may all cross it.
Steady flow: no property inside the CV changes with time.
  Mass balance (steady): ṁ₁ = ṁ₂ = ṁ = ρAV
Energy stored in the CV is constant → energy in = energy out.
CONTROL
VOLUME
ṁ, h₁, V₁, z₁
ṁ, h₂, V₂, z₂
Q̇ in
Ẇ out
Steady flow: mass in = mass out; properties inside do not change with time

## Slide 4
LECTURE 7 • TWO KEY IDEAS
Flow Work and Enthalpy
1
Flow work (flow energy)
To push 1 kg of fluid across the control surface against pressure p, the fluid behind must do work = p × v (pressure × specific volume). This energy rides with every kilogram that enters or leaves.
2
Total energy of a flowing stream
Per kg: internal energy u + flow work pv + kinetic energy V²/2 + potential energy gz.
3
Enthalpy — defined for convenience
h = u + pv (kJ/kg). It bundles internal energy with flow work, so a flowing stream simply carries h + V²/2 + gz.
4
Remember
Use u for non-flow (closed) energy storage, h for energy carried by flowing streams. This single habit prevents most open-system errors.
KEY POINT h = u + pv is a PROPERTY — it exists for stationary fluids too; it just becomes most useful in flow.

## Slide 5
LECTURE 7 • THE MASTER EQUATION
Steady Flow Energy Equation (SFEE)
Energy entering the CV per unit time = Energy leaving per unit time (steady state):
Q̇ − Ẇ = ṁ [ (h₂ − h₁) + (V₂² − V₁²)/2 + g(z₂ − z₁) ]
Rate form — W and Q in kW, ṁ in kg/s
q − w = (h₂ − h₁) + (V₂² − V₁²)/2000 + g(z₂ − z₁)/1000
Per unit mass, everything in kJ/kg (V in m/s, z in m)
Derivation logic (write these five lines in the exam)
1. Steady state ⇒ energy content of CV is constant.
2. Energy in: Q̇ + ṁ(h₁ + V₁²/2 + gz₁). 3. Energy out: Ẇ + ṁ(h₂ + V₂²/2 + gz₂).
4. Equate and rearrange → SFEE. 5. State assumptions: steady, 1-D flow, no storage.
KEY POINT V²/2 is in J/kg; divide by 1000 before adding to h in kJ/kg. Forgetting this factor is error #1 in CATs.

## Slide 6
LECTURE 7 • BOARD EXAMPLE
Computing Enthalpy and Flow Work
PROBLEM Steam flows in a pipeline at 800 kPa. At a section, its specific volume is 0.24 m³/kg and specific internal energy is 2576 kJ/kg. Find the flow work per kg and the specific enthalpy of the steam.
Solution
Flow work per kg = p v = 800 kPa × 0.24 m³/kg
p v = 192 kJ/kg
Enthalpy: h = u + p v = 2576 + 192
h = 2768 kJ/kg
ANSWER
pv = 192 kJ/kg
h = 2768 kJ/kg
KEY POINT kPa × m³/kg = kJ/kg. Steam-table enthalpies (Unit III) are built exactly this way.

## Slide 7
LECTURE 7 • HOUSEKEEPING
SFEE Term-by-Term: Meaning and Units
Term | Physical meaning | Unit (per-mass form)
q | Heat transfer to the fluid per kg | kJ/kg
w | Shaft work done by the fluid per kg | kJ/kg
h₂ − h₁ | Change in enthalpy (u + pv) | kJ/kg
(V₂² − V₁²)/2000 | Change in kinetic energy | kJ/kg (V in m/s)
g(z₂ − z₁)/1000 | Change in potential energy | kJ/kg (z in m)
KEY POINT For gases, gΔz is almost always negligible; drop it unless elevations are given.

## Slide 8
SESSION 9 • LECTURE 7 • WRAP-UP
Summary & What Comes Next
Today we covered
Open system → control volume with mass crossing the control surface
Flow work per kg = pv — the work needed to push fluid across the boundary
Enthalpy h = u + pv absorbs flow work into one property
SFEE (per kg): q − w = (h₂−h₁) + (V₂²−V₁²)/2 + g(z₂−z₁)
KE term in J/kg: divide V²/2 by 1000 to get kJ/kg — the classic slip
NEXT CLASS
Lecture 8 — SFEE Applications
Nozzle, turbine, compressor, boiler, condenser and throttling.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 5 (First Law Applied to Flow Processes)