## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 10 • LECTURE 8
Steady Flow Processes — Applications of the SFEE
Nozzles, diffusers, turbines, compressors, heat exchangers and throttling devices
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 10 • LECTURE 8
Session Outline
1
Recall & connect
SFEE per-unit-mass form on the board
2
Nozzle & diffuser
Enthalpy ↔ kinetic energy; exit-velocity formula
3
Turbine & compressor
Work devices; which terms vanish and why
4
Boiler, condenser, throttle
Heat devices and the h₁ = h₂ throttling result
5
Two board examples
Steam turbine power; cooled air compressor with velocities

## Slide 3
LECTURE 8 • THE DEVICE CATALOGUE
Simplified SFEE for Common Devices
Device | Valid assumptions | Simplified SFEE (per kg)
Nozzle / Diffuser | q ≈ 0, w = 0, ΔPE = 0 | (V₂²−V₁²)/2 = h₁ − h₂
Turbine | q ≈ 0, ΔKE ≈ 0, ΔPE ≈ 0 | w = h₁ − h₂ (> 0, work output)
Compressor / Pump | q ≈ 0, ΔKE ≈ 0, ΔPE ≈ 0 | w = h₁ − h₂ (< 0, work input)
Boiler / Evaporator | w = 0, ΔKE ≈ 0, ΔPE ≈ 0 | q = h₂ − h₁ (> 0, heat added)
Condenser / Cooler | w = 0, ΔKE ≈ 0, ΔPE ≈ 0 | q = h₂ − h₁ (< 0, heat rejected)
Throttling valve | q ≈ 0, w = 0, ΔKE ≈ 0 | h₁ = h₂ (isenthalpic)
KEY POINT Do not memorise six equations — memorise ONE (the SFEE) and the art of cancelling terms.

## Slide 4
LECTURE 8 • VELOCITY DEVICES
Nozzle and Diffuser — Trading h for Kinetic Energy
N
Nozzle
Flow area decreases (subsonic)
Pressure & enthalpy fall, velocity rises
V₂ = √(2000(h₁−h₂) + V₁²) m/s
h in kJ/kg inside the root
Steam turbines, jet engines, rockets
D
Diffuser
Exact reverse of a nozzle
Velocity falls, pressure & enthalpy rise
Used to recover pressure from a fast stream
Jet-engine intakes, centrifugal compressors
∑
Energy story
No work, no heat, no elevation change
Enthalpy + KE = constant along the device
Pure conversion between h and V²/2
h + V²/2000 = constant (kJ/kg)

## Slide 5
LECTURE 8 • BOARD EXAMPLE 1
Steam Turbine Power Output
PROBLEM Steam enters a turbine at h₁ = 3230 kJ/kg, V₁ = 50 m/s and leaves at h₂ = 2675 kJ/kg, V₂ = 120 m/s. Heat loss to surroundings is 8 kJ/kg; elevation change is negligible. For ṁ = 2.5 kg/s, find the power developed.
Solution
SFEE: q − w = (h₂−h₁) + (V₂²−V₁²)/2000
ΔKE = (120² − 50²)/2000 = (14400 − 2500)/2000 = 5.95 kJ/kg
q = −8 kJ/kg (loss). So: −8 − w = (2675 − 3230) + 5.95 = −549.05
w = −8 + 549.05 = 541.05 kJ/kg
Power = ṁ w = 2.5 × 541.05 = 1352.6 kW ≈ 1.35 MW
ANSWER
w ≈ 541 kJ/kg
Power ≈ 1.35 MW
KEY POINT Kinetic-energy change (5.95) is tiny beside Δh (555) — this is why turbines often neglect ΔKE.

## Slide 6
LECTURE 8 • BOARD EXAMPLE 2
Cooled Air Compressor with Velocity Change
PROBLEM Air flows steadily through a compressor at 0.5 kg/s. Enthalpy rises from 300 kJ/kg to 460 kJ/kg; velocity rises from 60 m/s to 120 m/s; heat rejected to cooling water is 25 kJ/kg. Find the power input.
Solution
ΔKE = (120² − 60²)/2000 = (14400 − 3600)/2000 = 5.4 kJ/kg
SFEE: q − w = Δh + ΔKE ⇒ w = q − Δh − ΔKE
w = (−25) − 160 − 5.4 = −190.4 kJ/kg (work input)
Power input = ṁ |w| = 0.5 × 190.4 = 95.2 kW
ANSWER
w = −190.4 kJ/kg
Power input ≈ 95.2 kW
KEY POINT Compressor w always comes out negative — quote the magnitude with the word "input".

## Slide 7
LECTURE 8 • HEAT & THROTTLE DEVICES
Boiler, Condenser and the Throttling Valve
1
Boiler / evaporator
Long tube bank, no shaft: q = h₂ − h₁ > 0. All heat goes into raising enthalpy (water → steam).
2
Condenser
Same balance with q < 0: steam surrenders its latent enthalpy to cooling water. ΔKE negligible in both.
3
Throttling device
Flow through a restriction (partially open valve, porous plug, capillary): q ≈ 0, w = 0, ΔKE ≈ 0 ⇒ h₁ = h₂.
4
Why throttling matters
Pressure drops at constant enthalpy; for real gases temperature usually drops too (Joule–Thomson effect, Unit IV) — the principle behind your refrigerator’s expansion valve.
KEY POINT Throttling is isenthalpic (h₁ = h₂) but NOT isothermal, and it is highly irreversible.

## Slide 8
SESSION 10 • LECTURE 8 • WRAP-UP
Summary & What Comes Next
Today we covered
Every device = SFEE with the right terms struck out
Nozzle: V₂ = √(2000(h₁−h₂)) m/s when V₁ is negligible
Turbine: w = h₁ − h₂ (positive); Compressor: w = h₁ − h₂ (negative → input)
Boiler/condenser: q = h₂ − h₁, no work
Throttling: h₁ = h₂ — isenthalpic, used in refrigerator expansion valves
NEXT CLASS
Lecture 9 — Unsteady Flow Processes
Filling and emptying of tanks — when “steady” no longer holds.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 5 (First Law Applied to Flow Processes)