## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 11 • LECTURE 9
Unsteady Flow Processes — Filling and Emptying of Vessels
When mass and energy inside the control volume change with time
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 11 • LECTURE 9
Session Outline
1
Recall & connect
Where the steady-flow assumption breaks down
2
General unsteady balances
Mass and energy conservation in interval form
3
Charging (filling) a tank
Derivation of the classic result u₂ = h_line for an evacuated tank
4
Discharging a tank
Energy balance for emptying; qualitative behaviour
5
Two board examples
Filling temperature; discharge cooling of a receiver

## Slide 3
LECTURE 9 • GENERALISING
The Unsteady (Transient) Flow Energy Balance
1
When steady fails
Filling a cylinder, discharging an air receiver, starting up a boiler — mass and stored energy inside the CV change with time.
2
Mass balance over the interval
(m₂ − m₁)_CV = Σm_in − Σm_out, where states 1 and 2 are the initial and final states of the CV.
3
Energy balance over the interval
Q − W = (m₂u₂ − m₁u₁)_CV − Σ m_in h_in + Σ m_out h_out (neglecting KE and PE of the streams).
4
Uniform-flow idealisation
Properties of the stream at the inlet/exit are constant in time (h_in fixed by the supply line) — makes the integrals simple products.

## Slide 4
LECTURE 9 • THE CLASSIC CASE
Charging an Insulated, Evacuated Tank
Rigid, insulated tank, initially evacuated (m₁ = 0), connected to a large supply line at p_line, T_line.
Valve opened; gas rushes in until tank pressure = line pressure.
  Q = 0 (insulated), W = 0 (rigid), m_out = 0.
  Energy balance: 0 = m₂u₂ − m_in h_line, and m_in = m₂.
Result: u₂ = h_line
Ideal gas: c_v T₂ = c_p T_line ⇒ T₂ = γ T_line — the gas in the tank is HOTTER than the line!
TANK
m, u, T rise
with time
Supply line
pₗ, Tₗ, hₗ
Valve
Charging: mass flows in, no mass leaves;
final energy = initial energy + enthalpy carried in
KEY POINT For air (γ = 1.4) from a 300 K line: T₂ = 420 K. The flow work pv done pushing gas in becomes internal energy.

## Slide 5
LECTURE 9 • THE MIRROR CASE
Discharging (Emptying) a Vessel
1
Setup
A rigid tank at high pressure discharges through a valve to the surroundings or a low-pressure line. Now m_out > 0, m_in = 0.
2
Energy balance
Q − 0 = (m₂u₂ − m₁u₁) + m_out h_out, with h_out evaluated at the (falling) tank conditions.
3
Behaviour
For rapid (adiabatic) discharge, the gas remaining in the tank expands and COOLS — it behaves as if expanding isentropically: T₂/T₁ = (p₂/p₁)^((γ−1)/γ).
4
Everyday evidence
A deodorant can or cycle-pump valve becomes cold on rapid discharge — you have felt unsteady-flow thermodynamics.

## Slide 6
LECTURE 9 • BOARD EXAMPLE 1
Filling a Tank from a Line
PROBLEM An insulated rigid tank, initially evacuated, is connected to an air line at 600 kPa, 300 K. The valve is opened until the tank reaches 600 kPa. Take γ = 1.4. Find the final air temperature in the tank.
Solution
Insulated + rigid + evacuated → u₂ = h_line
Ideal gas: c_v T₂ = c_p T_line
T₂ = (c_p/c_v) T_line = γ T_line
T₂ = 1.4 × 300 = 420 K = 147 °C
ANSWER
T₂ = 420 K (147 °C)
KEY POINT Final pressure does not appear in the result — T₂ depends only on γ and T_line.

## Slide 7
LECTURE 9 • BOARD EXAMPLE 2
Cooling During Rapid Discharge
PROBLEM An air receiver at 800 kPa, 400 K discharges rapidly until its pressure falls to 400 kPa. Treating the air remaining inside as expanding reversibly and adiabatically (γ = 1.4), estimate its temperature.
Solution
Isentropic relation: T₂/T₁ = (p₂/p₁)^((γ−1)/γ)
Exponent: (γ−1)/γ = 0.4/1.4 = 0.2857
T₂ = 400 × (0.5)^0.2857 = 400 × 0.8203
T₂ = 328 K ≈ 55 °C — a drop of 72 K from 400 K.
ANSWER
T₂ ≈ 328 K
KEY POINT Charging heats the tank; discharging cools it — remember the pair as opposites for viva questions.

## Slide 8
SESSION 11 • LECTURE 9 • WRAP-UP
Summary & What Comes Next
Today we covered
Unsteady (transient) flow: mass and energy inside the CV change with time
Mass balance: (m₂ − m₁)_CV = m_in − m_out
Energy balance: Q − W = (m₂u₂ − m₁u₁)_CV − m_in h_in + m_out h_out
Charging an insulated evacuated tank: u₂ = h_line → T₂ = γ T_line for ideal gas
Rapid discharge: remaining gas cools as T₂/T₁ = (p₂/p₁)^((γ−1)/γ)
NEXT CLASS
Tutorial 3 — SFEE & Unsteady Flow Problems
Unit-I finale, followed by the revision map for CAT-I (Units I & II).
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 5 (First Law Applied to Flow Processes)