## Slide 1
ME23312
ENGINEERING THERMODYNAMICS
UNIT I – Basics, Zeroth and First Law
SESSION 12 • TUTORIAL 3
Tutorial 3: SFEE & Unsteady Flow — Unit I Finale
Worked problems on flow devices and tank charging + Unit-I revision map for CAT-I (Units I & II)
Dr. Anantha Raman L., M.E., Ph.D.
Associate Professor
Department of Mechanical Engineering
Rajalakshmi Institute of Technology, Chennai, Tamil Nadu.

## Slide 2
SESSION 12 • TUTORIAL 3
Session Outline
1
Equation recall
SFEE and unsteady balances on the board
2
Problem 1 — nozzle
Exit velocity from enthalpy drop
3
Problem 2 — compressor
Power input with heat loss
4
Problem 3 — tank charging
Unsteady energy balance application
5
Problem 4 + revision map
Boiler heat duty; CAT-I question pattern for Unit I

## Slide 3
TUTORIAL 3 • WORKED PROBLEM 1
Nozzle Exit Velocity
PROBLEM Steam enters a nozzle with negligible velocity and h₁ = 3000 kJ/kg, leaving with h₂ = 2762 kJ/kg. The process is adiabatic with no work. Find the exit velocity.
Solution
Nozzle SFEE: (V₂² − V₁²)/2 = h₁ − h₂, with V₁ ≈ 0
V₂ = √(2000 × (h₁ − h₂)) [h in kJ/kg]
V₂ = √(2000 × 238)
V₂ = √476000 = 690 m/s
ANSWER
V₂ ≈ 690 m/s
KEY POINT The 2000 converts kJ/kg to m²/s². Without it you get 21.8 m/s — absurdly low for a nozzle.

## Slide 4
TUTORIAL 3 • WORKED PROBLEM 2
Compressor Power Input
PROBLEM Air flows steadily through a compressor at 0.8 kg/s. Enthalpy rises from 300 kJ/kg to 510 kJ/kg, and heat lost to cooling water is 40 kJ/kg. Neglect ΔKE and ΔPE. Find the power required.
Solution
SFEE: q − w = h₂ − h₁ (ΔKE = ΔPE = 0)
q = −40 kJ/kg (heat lost)
w = q − (h₂ − h₁) = −40 − 210 = −250 kJ/kg (input, as expected)
Power = ṁ |w| = 0.8 × 250 = 200 kW
ANSWER
w = −250 kJ/kg
Power input = 200 kW
KEY POINT Negative w from the algebra = work done ON the fluid. Report magnitude with the word "input".

## Slide 5
TUTORIAL 3 • WORKED PROBLEM 3
Charging a Tank (Unsteady Flow)
PROBLEM An insulated, rigid, evacuated bottle of 0.05 m³ is filled from an air line at 500 kPa, 290 K until pressures equalise. Take R = 0.287 kJ/kg·K, γ = 1.4. Find the final temperature and the mass of air that enters.
Solution
Charging result: T₂ = γ T_line = 1.4 × 290 = 406 K
Final state: p₂ = 500 kPa, V = 0.05 m³, T₂ = 406 K
m₂ = p₂V / (R T₂) = (500 × 0.05)/(0.287 × 406)
m₂ = 25 / 116.5 = 0.2146 kg
ANSWER
T₂ = 406 K
m ≈ 0.215 kg
KEY POINT pV = mRT with p in kPa, V in m³ and R in kJ/kg·K gives m in kg directly.

## Slide 6
TUTORIAL 3 • WORKED PROBLEM 4
Boiler Heat Duty
PROBLEM Feed water enters a boiler with h₁ = 505 kJ/kg and leaves as steam with h₂ = 2960 kJ/kg at a steady rate of 1.2 kg/s. Velocities and elevation changes are negligible and there is no shaft work. Find the rate of heat supply.
Solution
Boiler SFEE: q = h₂ − h₁ (w = 0, ΔKE = ΔPE = 0)
q = 2960 − 505 = 2455 kJ/kg
Q̇ = ṁ q = 1.2 × 2455
Q̇ = 2946 kW ≈ 2.95 MW
ANSWER
q = 2455 kJ/kg
Q̇ ≈ 2.95 MW
KEY POINT Boiler and condenser problems are pure enthalpy bookkeeping — easy full marks if the units are clean.

## Slide 7
TUTORIAL 3 • EXAM COMPASS
Unit-I Revision Map for CAT-I (Units I & II)
Topic block | Expected question type | Marks weight
Systems, properties, point/path functions | Definitions, 2-mark & MCQ | 2–4
Quasi-static & equilibrium | Short explanation with sketch | 2–4
Displacement work & p-V diagram | Numerical (polytropic / isothermal) | 8–13
Zeroth law & temperature scales | Statement + conversion numerical | 2–6
First law — closed system | Numerical (process or cycle table) | 8–13
SFEE derivation + device numerical | Derivation (8) or turbine/nozzle problem | 8–13
Unsteady flow (charging) | Short derivation or direct numerical | 4–8
KEY POINT CAT-I = Units I & II together. Priority: first-law numericals → SFEE → work integrals → theory definitions.

## Slide 8
SESSION 12 • TUTORIAL 3 • WRAP-UP
Summary & What Comes Next
Today we covered
Unit I complete: systems → equilibrium → work → zeroth law → first law (closed & open) → unsteady flow
SFEE devices: strike out terms, never memorise separately
Nozzle root formula needs the 2000 factor with h in kJ/kg
Charging result u₂ = h_line; discharging cools the tank
CAT-I covers Units I & II — revise both tutorial sheets and the Nag solved examples
NEXT CLASS
Unit II begins — Heat Engine, Refrigerator, Heat Pump
The second law enters: why 100% conversion of heat to work is impossible.
Text: P.K. Nag, "Engineering Thermodynamics", 6th Edn., TMH — Ch. 5 (First Law Applied to Flow Processes)